## Slide 1
Predicting Flank Wear in CNC Milling machine
presented by :
CHINTHALA PRAJAY VARMA 230003018
JAAJIMOGGALA RAMARAJU 230003028
BANOTH SANTHOSH 230003014

## Slide 2
Problem Statement
Problem Description
To monitor the flank wear of a CNC milling machine tool.
Sensor data:
  Spindle Motor Current (DC) sensor
  Vibration (Spindle) sensor
Key variables include:
  Case no., Run, VB (Flank wear), Time, Depth of Cut (DOC), Feed rate
Objectives
Investigate tool wear on a CNC milling machine.
Understand how various factors influence flank wear over time.
Use the training data to:
  Accurately predict flank wear.
  Identify key features contributing to the prediction of flank wear in the testing dataset.

## Slide 3
Data Preprocessing
For Score 1:
No changes were made to the data during the first submission.
For Score 2: Missing runs of VB were added by taking the average of the preceding and succeeding runs.
Feature Extraction
Training Dataset: 52 runs Testing Dataset: 57
Score 1 Approach:
Computed the mean of 9000 data samples for each run (both sensors).
This resulted in a single sensor value corresponding to VB for each run.
Attempts to use standard deviation increased error rates compared to the mean approach.

## Slide 4
Score 2 Approach:
For each run, data points were arranged in ascending order.
Removed the lowest and highest 1000 data points.
Computed the mean for the remaining 7000 data points.
Feature Set
Score 1
Score 2
Training Features
4 × 52 = 208
3 × 52 = 156
Testing Features
4 × 57 = 228
3 × 57 = 171
variables used
DC, VIB, Feed, DOC
DC, VIB, Time

## Slide 5
Model Training and Evaluation
Data Loading: Used readtable() to load the training and testing datasets.
Feature Extraction: Selected relevant variables:
  VIB, DC, DOC, Feed (Score 1)
  VIB, DC, Time (Score 2)
  Target variable: VB (Flank wear)
Model Training:
  Applied a Linear Regression Model using fitlm().
Performance Evaluation:
  Computed the Root Mean Square Error (RMSE) for training and testing datasets:{predictions_test = predict(lrModel, X_test); rmse_test = sqrt(mean((y_test - predictions_test).^2)); disp(['Linear Regression RMSE (test): ', num2str(rmse_test)]);}
5.Visualization:
  Generated a scatter plot comparing actual vs. predicted values for validation:{scatter(y_test, predictions_test, 'b', 'filled', 'DisplayName', 'Predicted vs Actual');}

## Slide 6
comparing models through visualization
linear regression model for score 1
linear regression model for score 2